## Slide 1: CCIE Enterprise Bootcamp
IPv6 Foundation

## Slide 2: IPv6 Addressing
As described in RFC 4291, the preferred form is x:x:x:x:x:x:x:x
  Each x is a 16-bit section

## Slide 3: IPv6 Addressing
RFC 2373 and RFC 5952 provide two helpful rules for reducing the notation involved in the preferred format
Rule 1: Omit Leading 0s
Rule 2: Omit All-0s Hextets
Combining Rule 1 and Rule 2

## Slide 4: IPv6 Addressing
IPv4, with its 32-bit address space, provides for 4.29 billion
IPv6 - 340,282,366,920,938,463,463,374,607,431,768,211,456 addresses

## Slide 5: IPv6 Addressing

## Slide 6: IPv6 Addressing

## Slide 7: IPv6 Unicast Adresses
Global unicast
Link-local
Loopback
Unspecified address
Unique local
IPv4 embedded

## Slide 8: Global Unicast Address
Global Routing Prefix
Subnet ID
Interface ID

## Slide 9: Link-Local Unicast Address

## Slide 10: Link-Local Unicast Address
device must have an IPv6 link-local address
Link-local addresses are not routable off the link
Link-local addresses only have to be unique on the link
There can be only one link-local address per interface

## Slide 11: Link-Local Unicast Address
Devices dynamically (automatically) create their own link-local IPv6 address upon startup
Link-local addresses can be manually configured
When a device starts up, before it obtains a GUA address, the device uses its IPv6 link-local address as its source address to communicate with other devices on the network
Devices use the router’s link-local address as their default gateway address
IPv6 routing table entries populated from dynamic routing protocols use the IPv6 link-local address as the next-hop address

## Slide 12: MULTICAST ADDRESSES

## Slide 13: Well-Known Multicast Addresses
ff02::1:
  All IPv6 devices
ff02::2:
  All IPv6 routers
ff02::5:
  All OSPFv3 routers
ff02::a:
  All EIGRP (IPv6) routers

## Slide 14: Solicited-Node Multicast Addresses
used as a more efficient approach to IPv4’s broadcast address
used in Layer 3-to-Layer 2 address resolution, similar to how Address Resolution Protocol (ARP) is used in IPv4
automatically created using a special mapping of the device’s unicast address with the solicited-node multicast prefix ff02:0:0:0:0:1:ff00::/104

## Slide 15: Dynamic Addressing
Method 1: Stateless Address Autoconfiguration (SLAAC)
Method 2: SLAAC and a stateless DHCPv6 server
Method 3: Stateful DHCPv6 server

## Slide 16: Method 1: SLAAC

## Slide 17: Method 2: stateless DHCPv6 server
! Configure the stateless DHCPv6 server pool R1(config)# ipv6 dhcp pool STATELESS-DHCPv6 R1(config-dhcpv6)# dns-server 2001:db8:cafe:1::8888 R1(config-dhcpv6)# domain-name example.com R1(config-dhcpv6)# exit ! Set the O flag to 1 and enable DHCPv6 service R1(config)# interface gigabitethernet 0/0 R1(config-if)# ipv6 nd other-config-flag R1(config-if)# ipv6 dhcp server STATELESS-DHCPv6 R1(config-if)#

## Slide 18: Method 3: Stateful DHCPv6
! Configure the stateful DHCPv6 server pool R1(config)# ipv6 dhcp pool STATEFUL-DHCPv6 R1(config-dhcpv6)# address prefix 2001:db8:cafe:1:deed::/80 R1(config-dhcpv6)# dns-server 2001:db8:cafe:1::8888 R1(config-dhcpv6)# domain-name example.com R1(config-dhcpv6)# exit ! Set the M flag to 1, the A flag to 0 and enable DHCPv6 service on the interface R1(config)# interface gigabitethernet 0/0 R1(config-if)# ipv6 nd managed-config-flag R1(config-if)# ipv6 nd prefix 2001:db8:cafe:1::/64 no-autoconfig R1(config-if)# ipv6 dhcp server STATEFUL-DHCPv6

## Slide 19: ICMPv6 Neighbor Discovery
Router–device messages used for dynamic address allocation:
  Router Solicitation (RS) message
  Router Advertisement (RA) message
Device–device messages used for address resolution:
  Neighbor Solicitation (NS) message
  Neighbor Advertisement (NA) message
Router–device messages used for better first-hop selection:
  Redirect message

## Slide 20: Router Solicitation Message
A host sends a Router Solicitation message when it needs to know how to dynamically obtain its addressing information. This typically occurs during startup and is the default on most host operating systems

## Slide 21: Router Advertisement Message
A Cisco router sends Router Advertisement messages every 200 seconds The RA message is a suggestion to obtain addressing information dynamically. This information in the RA message includes prefix, default router, and other configuration information

## Slide 22: Neighbor Solicitation