## Slide 1: OSPFv3 Address Family Mode в Cisco IOS

## Slide 2: OSPFv3 Address Family Mode
OSPFv3 очень похож на OSPFv2
  Синтаксис Classic Mode наследуется для совместимости
  Настраивается в разных частях конфигурационного файла
  Разный синтаксис некоторых команд настройки IPv4 и IPv6
AF Mode – альтернативный синтаксис настройки OSPFv3
  Протокол тот же самый, разница только в конфигурации
  Позволяет синхронизировать маршрутные таблицы IPv4 и IPv6
    Каждое адресное семейство работает в отдельном Instance
    Пакеты OSPFv3 в любом случае бегают поверх IPv6
Конфигурируется с нуля или импортирует конфиг Classic Mode
  Настройки интерфейсов и команды работают в обоих синтаксисах
  Обращение к новому синтаксису автоматически обновляет конфигурацию

## Slide 3: Включение OSPFv3
Для работы OSPFv3 требуется включение IPv6 на интерфейсе
  Для синхронизации AF IPv4 не требуется включение AF IPv6
  Настройки можно задавать как на адресное семейство, так и на весь роутер
G0/0
G0/0
F0/0
F0/1 F0/2
R1(config)#router ospfv3 1
R1(config-router)#address-family ipv4
R1(config-router-af)#router-id 0.0.0.1
R1(config-router)#address-family ipv6
R1(config-router-af)#router-id 0.0.0.1
R1(config)#interface GigabitEthernet0/0
R1(config-if)#ip address 192.168.1.1 255.255.255.0
R1(config-if)#ipv6 enable
R1(config-if)#ospfv3 1 ipv4 area 0
*Mar 26: %OSPFv3-5-ADJCHG: Process 1, IPv4, Nbr 0.0.0.2 on GigabitEthernet0/0 from LOADING to FULL, Loading Done
R1(config-if)#ospfv3 1 ipv6 area 0
*Mar 26: %OSPFv3-5-ADJCHG: Process 1, IPv6, Nbr 0.0.0.2 on GigabitEthernet0/0 from LOADING to FULL, Loading Done
R1
R2

## Slide 4: Источники маршрутной информации
Диагностика подсистемы маршрутизации
Router#show ip protocols | section ospf
Routing Protocol is "ospfv3 1"
Outgoing update filter list for all interfaces is not set
Incoming update filter list for all interfaces is not set
Router ID 0.0.0.1
Number of areas: 1 normal, 0 stub, 0 nssa
Interfaces (Area 0):
GigabitEthernet0/0
Maximum path: 4
Routing Information Sources:
Gateway Distance Last Update
0.0.0.2 110 00:02:02
Distance: (default is 110)
Router#show ipv6 protocols | section ospf
IPv6 Routing Protocol is "ospf 1"
Router ID 0.0.0.1
Number of areas: 1 normal, 0 stub, 0 nssa
Interfaces (Area 0):
GigabitEthernet0/0
Redistribution:
None

## Slide 5: Диагностика процесса OSPFv3 AF Mode
Диагностика протокола
Router#show ospfv3
OSPFv3 1 address-family ipv4
Router ID 0.0.0.2
Supports NSSA (compatible with RFC 3101)
Event-log enabled, Maximum number of events: 1000, Mode: cyclic
Router is not originating router-LSAs with maximum metric
Initial SPF schedule delay 5000 msecs
Minimum hold time between two consecutive SPFs 10000 msecs
Maximum wait time between two consecutive SPFs 10000 msecs
Minimum LSA interval 5 secs
Minimum LSA arrival 1000 msecs
LSA group pacing timer 240 secs
Interface flood pacing timer 33 msecs
Retransmission pacing timer 66 msecs
Retransmission limit dc 24 non-dc 24
Number of external LSA 0. Checksum Sum 0x000000
Number of areas in this router is 1. 1 normal 0 stub 0 nssa
Graceful restart helper support enabled
Reference bandwidth unit is 100 mbps
RFC1583 compatibility enabled
Area BACKBONE(0)
Number of interfaces in this area is 3
SPF algorithm executed 2 times
Number of LSA 7. Checksum Sum 0x03F211
Number of DCbitless LSA 0
Number of indication LSA 0
Number of DoNotAge LSA 0
Flood list length 0
OSPFv3 1 address-family ipv6
Router ID 0.0.0.2
Supports NSSA (compatible with RFC 3101)
Event-log enabled, Maximum number of events: 1000, Mode: cyclic
Router is not originating router-LSAs with maximum metric
Initial SPF schedule delay 5000 msecs
Minimum hold time between two consecutive SPFs 10000 msecs
Maximum wait time between two consecutive SPFs 10000 msecs
Minimum LSA interval 5 secs
Minimum LSA arrival 1000 msecs
LSA group pacing timer 240 secs
Interface flood pacing timer 33 msecs
Retransmission pacing timer 66 msecs
Retransmission limit dc 24 non-dc 24
Number of external LSA 4. Checksum Sum 0x021ABB
Number of areas in this router is 1. 1 normal 0 stub 0 nssa
Graceful restart helper support enabled
Reference bandwidth unit is 100 mbps
RFC1583 compatibility enabled
Area BACKBONE(0)
Number of interfaces in this area is 2
SPF algorithm executed 2 times
Number of LSA 17. Checksum Sum 0x09E6A3
Number of DCbitless LSA 0
Number of indication LSA 0
Number of DoNotAge LSA 0
Flood list length 0

## Slide 6: Базовая диагностика OSPFv3 AF Mode
Проверка интерфейсов, включая пассивные
Проверка соседств (для IPv6 – show ospfv3 ipv6 neighbor)
Проверка таблицы маршрутизации (show ip route ospf не работает)
Router#show ospfv3 ipv4 interface brief
Interface PID Area AF Cost State Nbrs F/C
Gi0/0 1 0 ipv4 1 BDR 1/1
Router#show ospfv3 ipv6 interface brief
Interface PID Area AF Cost State Nbrs F/C
Gi0/0 1 0 ipv6 1 BDR 1/1
Router#show ospfv3 ipv4 neighbor
OSPFv3 1 address-family ipv4 (router-id 10.1.2.1)
Neighbor ID Pri State Dead Time Interface ID Interface
0.0.0.2 1 FULL/DR 00:00:36 3 GigabitEthernet0/0
Router#show ip route ospfv3 | section \[110
O 2.2.2.2 [110/10] via 10.1.2.2, 00:15:44, GigabitEthernet0/0
Router#show ipv6 route ospf | section \[110
O FD00::/16 [110/20]
via FE80::A8BB:CCFF:FE00:410, GigabitEthernet0/0

## Slide 7: Конфигурация интерфейсов (1)
Можно задать стоимость интерфейса в явном виде или изменить референсную полосу для автоматического подсчета стоимости
  Для отдельного адресного семейства или всех семейств протокола
Настройка пассивных интерфейсов предсказуема
R1(config)#router ospfv3 1
R1(config-router)#auto-cost reference-bandwidth 100
R1(config-router)#address-family ipv4
R1(config-router-af)#auto-cost reference-bandwidth 200
R1(config-router-af)#interface GigabitEthernet0/0
R1(config-if)#ospfv3 cost 10
R1(config-if)#ospfv3 1 ipv4 cost 15
R1(config)#router ospfv3 1
R1(config-router)#passive-interface default
R1(config-router)#no passive-interface GigabitEthernet0/0
R1(config-router)#address-family ipv4
R1(config-router-af)#no passive-interface default
R1(config-router-af)#passive-interface GigabitEthernet0/0

## Slide 8: Конфигурация интерфейсов (2)
Приоритет DR/BDR и выбор канальной среды независимы для AF
Router(config-if)#ospfv3 priority 1
Router(config-if)#ospfv3 1 ipv4 priority 2
Router(config-if)#ospfv3 hello-interval 10
Router(config-if)#ospfv3 1 ipv4 hello-interval 5
Router(config-if)#ospfv3 dead-interval 40
Router(config-if)#ospfv3 1 ipv4 network broadcast
Router(config-if)#ospfv3 1 ipv6 network nonbroadcast
Router(config-if)#ospfv3 neighbor fe80::2

## Slide 9: Диагностика OSPFv3 AF Mode
Диагностика интерфейса: show ospfv3 <#> <AF> interface <IF>
Диагностика соседства: show ospfv3 <#> <AF> neighbor <IF> <ID>
Просмотр LSDB: show ospfv3 <#> <AF> database

## Slide 10: Диагностика LSDB
Просмотр таблицы LSDB для AF IPv4
R1#show ospfv3 1 ipv4 database
OSPFv3 1 address-family ipv4 (router-id 0.0.0.1)
Router Link States (Area 0)
ADV Router Age Seq# Fragment ID Link count Bits
0.0.0.1 109 0x80000006 0 1 None
0.0.0.2 44 0x80000007 0 1 B
Inter Area Prefix Link States (Area 0)
ADV Router Age Seq# Prefix
0.0.0.2 34 0x80000001 2.2.2.2/32
Link (Type-8) Link States (Area 0)
ADV Router Age Seq# Link ID Interface
0.0.0.1 110 0x80000001 3 Et0/0
0.0.0.2 860 0x80000003 3 Et0/0
Intra Area Prefix Link States (Area 0)
ADV Router Age Seq# Link ID Ref-lstype Ref-LSID
0.0.0.1 109 0x80000001 0 0x2001 0
0.0.0.2 44 0x80000007 0 0x2001 0
.1
1.1.1.1/32
.2
2.2.2.2/32
OSPF area 0
OSPF area 1
0.0.0.1
0.0.0.2

## Slide 11: Диагностика Link LSA
Просмотр отдельной Link LSA
R1#show ospfv3 1 ipv4 database link interface GigabitEthernet0/0 adv-router 0.0.0.1
OSPFv3 1 address-family ipv4 (router-id 0.0.0.1)
Link (Type-8) Link States (Area 0)
LS age: 1189
Options: (E-Bit, R-Bit, DC-Bit, AF-Bit)
LS Type: Link-LSA (Interface: Ethernet0/0)
Link State ID: 3 (Interface ID)
Advertising Router: 0.0.0.1
LS Seq Number: 8000001C
Checksum: 0xF6C3
Length: 52
Router Priority: 1
Link Local Address: 10.1.2.1
Number of Prefixes: 1
Prefix Address: 10.1.2.0
Prefix Length: 24, Options: None
.1
1.1.1.1/32
.2
2.2.2.2/32
OSPF area 0
OSPF area 1
0.0.0.1
0.0.0.2

## Slide 12: Диагностика Intra-Area Prefix LSA
Просмотр отдельной Intra-Area Prefix LSA
R1#show ospfv3 1 ipv4 database prefix adv-router 0.0.0.1
OSPFv3 1 address-family ipv4 (router-id 0.0.0.1)
Intra Area Prefix Link States (Area 0)
Routing Bit Set on this LSA
LS age: 199
LS Type: Intra-Area-Prefix-LSA
Link State ID: 0
Advertising Router: 0.0.0.1
LS Seq Number: 80000001
Checksum: 0x39A0
Length: 40
Referenced LSA Type: 2001
Referenced Link State ID: 0
Referenced Advertising Router: 0.0.0.1
Number of Prefixes: 1
Prefix Address: 1.1.1.1
Prefix Length: 32, Options: None, Metric: 10
.1
1.1.1.1/32
.2
2.2.2.2/32
OSPF area 0
OSPF area 1
0.0.0.1
0.0.0.2

## Slide 13: Диагностика Inter-Area Prefix LSA
Просмотр отдельной Inter-Area Prefix LSA
R1#show ospfv3 1 ipv4 database inter-area prefix 2.2.2.2
OSPFv3 1 address-family ipv4 (router-id 0.0.0.1)
Inter Area Prefix Link States (Area 0)
Routing Bit Set on this LSA
LS age: 173
LS Type: Inter Area Prefix Links
Link State ID: 0
Advertising Router: 0.0.0.2
LS Seq Number: 80000001
Checksum: 0xE828
Length: 32
Metric: 0
Prefix Address: 2.2.2.2
Prefix Length: 32, Options: None
.1
1.1.1.1/32
.2
2.2.2.2/32
OSPF area 0
OSPF area 1
0.0.0.1
0.0.0.2

## Slide 14: Что бы подебажить?
Hello protocol
Обмен пакетами
Построение LSDB и пересчет SPF
Router#debug ospfv3 hello
*Mar 25 19:18:05.873: OSPFv3-1-IPv4 HELLO Et0/0: Rcv hello from 0.0.0.2 area 0 from FE80::2 interface ID 3
*Mar 25 19:18:08.306: OSPFv3-1-IPv6 HELLO Gi0/0: Rcv hello from 0.0.0.2 area 0 from FE80::2 interface ID 3
*Mar 25 19:18:08.360: OSPFv3-1-IPv6 HELLO Gi0/0: Mismatched hello parameters from 0.0.0.2
Router#debug ospfv3 packet
*Mar 25 19:20:31.743: OSPFv3-1-IPv6 PAK Gi0/0: rcv. v:3 t:2 l:228 rid:0.0.0.2
*Mar 25 19:20:31.743: OSPFv3-1-IPv6 PAK Gi0/0: aid:0.0.0.0 chk:CE7B inst:0 from GigabitEthernet0/0
Router#debug ospfv3 spf ?
external SPF for external routes
inter SPF for inter-area routes
intra SPF for intra-area routes
statistic SPF statistics
<cr>

## Slide 15: Stub, default route, редистрибуция
Настройка регионов идентична Classic Mode
Импорт default route и редистрибуция выполняются в контексте AF
Virtual Link
Router(config)#router ospfv3 1
Router(config-router)#area 2 stub
Router(config-router)#area 3 stub no-summary
Router(config-router)#area 4 nssa
Router(config-router)#area 5 nssa no-summary default-information-originate metric 15 metric-type 1
Router(config-router)#area 5 nssa translate type7 always suppress-fa
R1(config)#router ospfv3 1
R1(config-router)#address-family ipv4
R1(config-router-af)default-information originate always metric 25 metric-type 1
R1(config-router-af)#redistribute connected
R1(config-router-af)#redistribute static metric 10 metric-type 1 tag 123
R1(config-router-af)#redistribute eigrp 1 include-connected route-map EIGRP_TO_OSPF
R1(config-router-af)#default-metric 25
R2(config)#router ospf 1
R1(config-router)#address-family ipv4
R2(config-router-af)#area 1 virtual-link 1.1.1.1

## Slide 16: Distribute-list в OSPFv3 AF Mode
В AF IPv4 работает с prefix-list, gateway и ACL (но не route-map)
RIB
OSPF
BGP
Router(config)#router ospfv3 1
Router(config-router)#address-family ipv4
Router(config-router-af)#distribute-list ?
<1-199> IP access list number
<1300-2699> IP expanded access list number
WORD Access-list name
gateway Filtering incoming updates based on gateway
prefix Filter prefixes in routing updates
Router(config-router-af)#address-family ipv6
Router(config-router-af)#distribute-list ?
prefix-list Filter connections based on an IPv6 prefix-list

## Slide 17: Агрегация маршрутов OSPFv3
Агрегация inter-area маршрутов на ABR
  Метрика агрегата – максимальная метрика его компонентов
Агрегация external маршрутов на ASBR:
Router(config)#router ospfv3 1
Router(config-router)#address-family ipv4
Router(config-router-af)#summary-prefix 192.168.0.0/16
Router(config-router)#address-family ipv4
Router(config-router-af)#summary-prefix fd00::/16
Router(config)#router ospfv3 1
Router(config-router)#address-family ipv4
Router(config-router-af)#area 1 range 10.1.0.0 255.255.0.0
Router(config-router)#address-family ipv4
Router(config-router-af)#area 1 range fd00:1::/32

## Slide 18: Манипуляции с AD
Административное расстояние задается на адресное семейство
  Значения по умолчанию такие же, как в OSPFv2: 110/110/170
  distance <#> задает все три значения
  distance ospf позволяет задать отдельные значения
  Отдельным маршрутам AD переопределить нельзя
Router(config)#router ospfv3 1
Router(config-router)#address-family ipv6
Router(config-router-af)#distance ospf intra-area 120 inter-area 125 external 160
Router(config-router-af)#do show ipv6 route ospf | section ::
O FD00::1/128 [120/10]
via FE80::2, GigabitEthernet0/0
OI FD00::2/128 [125/20]
via FE80::2, GigabitEthernet0/0
OE1 FD00::3/128 [160/131], tag 1
via FE80::2, GigabitEthernet0/0

## Slide 19: OSPFv3 AF Mode и IPsec
AF Mode поддерживает аутентификацию IPsec только на интерфейсе
Кроме того, поддерживается Authentication Trailer
Authentication Trailer поддерживает настройку на уровне региона
Router(config-if)#ospfv3 authentication ipsec spi 500 md5 1234567890abcdef1234567890abcdef
Router(config-if)#ospfv3 1 ipv4 authentication ipsec spi 500 sha1 1234567890123456789012345678901234567890
Router(config-if)#ospfv3 encryption ipsec spi 500 esp aes-cbc 128 1234567890abcdef1234567890abcdef sha1 1234567890123456789012345678901234567890
R1(config)#key chain OSPF_KEYCHAIN
R1(config-keychain)#key 1
R1(config-keychain-key)#cryptographic-algorithm hmac-sha-256
R1(config-keychain-key)#key-string SECRETKEY
R1(config-keychain-key)#interface GigabitEthernet0/0
R1(config-if)#ospfv3 authentication key-chain OSPF_KEYCHAIN
Router(config)#router ospfv3 1
Router(config-router)#area 1 authentication key-chain OSPF_KEYCHAIN